## Slide 1: Microphone arrays and virtual microphones
A.Farina, A. Capra
New trends in
audio processing
and rendering
New opportunities for the
audio industry
Milano, Nov. 21, 2011
FAST - Sala Morandi
Piazzale R. Morandi 2, Milano
Industrial Engineering Dept.
University of Parma, Italy
farina@unipr.it

## Slide 2
GOALS
We want to synthesize virtual microphones, highly directive, steerable, and with variable directivity pattern

## Slide 3: Previous experience
At UNIPR we have 15+ years of experience employing 1st-order Ambisonics microphones (Soundfield TM, DPA-4, Tetramic, Brahma)
3
Notes: Innovazioni Tecnologiche Audio
01/03/2010
Leonardo Scopece
3
Nuove tecnologie
06/03/2009
Leonardo Scopece
3

## Slide 4: Capturing Ambisonics signals
A tetrahedrical microphone probe was developed by Gerzon and Craven, originating the Soundfield microphone, in 1973
The Acoustics of Ancient Theatres Conference

## Slide 5: Soundfield microphones
The Acoustics of Ancient Theatres Conference

## Slide 6: Ambisonics signals
The Soundfield (TM) microphone provides 4 signals: 1 omnidirectional (pressure, W) and 3 figure-of-8 (velocity, X, Y, Z)

## Slide 7: Directivity of transducers
Soundfield ST-250 microphone

## Slide 8: Current use of Ambisonics
1st order Ambisonics is still widely employed for room acoustics (impulse response) measurements
It can be implemented employing very cheap equipment (Tetramic, Brahma)
Pulsive sound sources are usually preferred for a number of reasons
Portable, battery operated recorders make it very easy to collect a large number of impulse responses
A new digital method of processing the signals provides much better polar response than those available form the original Soundfield microphone

## Slide 9: Current use of Ambisonics
A portable digital recorder equipped with tetrahedrical microphone probe: BRAHMA

## Slide 10: Current use of Ambisonics
Balloons or Firecrackers as sound source

## Slide 11: Conversion from A-format to B-format
4 outputs
X-Volver
4 inputs

## Slide 12: ISO 3382 acoustical parameters
Aurora plugin – processing the Odeion in Patra

## Slide 13: Spatial Analysis
The direction of arrival can be found as follows:
The Sound Intensity vector components are computed
Ix=w·x Iy=w·y Iz=w·z
Also the total energy density is computed
De =
√(w2+x2+y2+z2)
They are averaged over 1ms time slices
The ratio between active intensity and energy density is finally computed
│I│ = sqrt(Ix2 + Iy2 + Iz2) R= │I│/ De
And azimuth and elevation of reflections are found:
Az = atan2(Iy,Ix) El = asin( Iz / │I│)

## Slide 14: Background image
The Mercator projection is employed for creating a rectangular image covering the whole surface of the sphere

## Slide 15: Image Composite Editor
Creates a panoramic image ranging 360°horizontally and up to 180°vertically

## Slide 16: Reflection Mapping
We can now plot a circle for every reflection, at the Azimuth and Elevation found, over a standard Cartesian framework
The radius of the circle is made proportional to the Sound Intensity level in dB
The transparency of the circle is made proportional to the ratio R
When R is low, the intensity is not indicating anymore a direction of arrival which can be perceived by the listeners
When R is large (close to 1), the sound is strongly polarized in one direction, which can be easily perceived

## Slide 17: Echo localization from B-format IR
Visual Basic program for displaying reflections
Sound Intensity
Energy Density

## Slide 18: Echo localization from B-format IR
Visual Basic program for displaying reflections - video

## Slide 19: Massive microphone arrays
Thanks to the recent availability of a massive 32-capsules spherical microphone array (Eigenmike™), it is now possible to synthesize high directivity virtual microphones, thanks to three competing technologies:
HOA: High Order Ambisonics (3rd order B-format)
Direct numerical synthesis (Matrix of FIR filters)
SPS: Spatial PCM Sampling (NEW !!!)

## Slide 20
Spherical arrays
2009: first prototype of a spherical array (32 capsules)
Expanded polyurethane
(too much delicate for handling!)
32 capsules for earing-aid
(poor quality)
Notes: A shotgun microphone comports a waste of time for covering all the directions on the hemisphere, changing more than one point of measure inside the theatre. For this reason we tried with a different approach employing a microphone array.
20

## Slide 21
2010: The EIGENMIKE/32TM
Array with 32 ½” capsules of excellent quality, frequency response up to 20 kHz
Preamplifiers and A/D converters inside the sphere, with ethernet interface
Processing on the PC thanks to a VST plugin (no GUI)
21
Cat5 cable

## Slide 22
2022: The EIGENMIKE-64/TM
Array with 64 10mm capsules of high quality, frequency response up to 20 kHz
Preamplifiers and A/D converters inside the sphere, with Dante interface
Processing on the PC thanks to a VST plugin (no GUI)
Ambisonics up to order 6 (49 channels)
22
POE powerbank
Cat5 cable
Cat5 cable

## Slide 23
1) Spherical Harmonics approach
Spherical Harmonics (H.O.Ambisonics)
A fixed number of “intermediate” virtual microphones is computed (3rd order B-format), then the dynamically-positioned virtual microphones are obtained by linear combination of these intermediate signals. This limits both dynamic range and frequency range.
Virtual microphones

## Slide 24: HOA software
The Eigenmike-32 is sold accompanied by this software tool, capable of synthesizing up to 16 virtual microphones, working by means of 3rd-order Ambisonics

## Slide 25: HOA software
The Eigenmike-64 is sold accompanied by this software tool, capable of synthesizing up to 32 virtual microphones, working by means of 6th-order Ambisonics

## Slide 26: Problems with HOA
50% of the spatial information is lost (32 channels are squeezed to 16 3rd order spherical harmonics)
High order harmonics have very limited usable frequency range
At low frequency, a lot of noise appears
The virtual microphones being synthesized have frequency-dependent polar patterns (with lesser directivity at low and very high frequency)
The frequency range is limited to 10 kHz
The supplied software is unpractical, as the user does not “see” where each virtual microphone is aimed to.

## Slide 27
2) Direct numerical synthesis
The idea
Direct synthesis of 32 directive virtual microphones in the direction of the capsules employing a set of digital filters
M = 32 signals coming from the capsules
V = 32 signals yielding the desired virtual microphones
Bank of MxV FIR filters
Output signal of V mics.
Input signals from the M capsules
Matrix of filters
Notes: The idea is to synthetize 32 directive virtual microphones in the direction of the capsules employing a set of digital filters.
We have 32 signals coming from the capsules and we desire 32 signals yielding the virtual microphones: so we need a bank of MxV FIR filters.
The convolution of the inputs with the filters gives as output the virtual microphone.
27

## Slide 28: Novel approach
No theory is assumed: the set of hm,v filters are derived directly from a set of impulse response measurements, designed according to a least-squares principle.
In practice, a matrix of impulse responses is measured, and the matrix has to be numerically inverted (usually employing some regularization technique).
This way, the outputs of the microphone array are maximally close to the ideal responses prescribed
This method also inherently corrects for transducer deviations and acoustical artifacts (shielding, diffractions, reflections, etc.)

## Slide 29
The microphone array impulse responses cm,d , are measured for a number of D incoming directions.
We get a matrix C of measured impulse responses for a large number D of directions
m=1…M mikes
d=1…D sources
cki
Novel approach

## Slide 30: Target Directivity
The virtual microphone which we want to synthesize must be specified in the same D directions where the impulse responses had been measured. Let’s choose a high-order cardioid of order n as our target virtual microphone.
This is just a direction-dependent gain. The theoretical impulse response coming from each of the D directions is:

## Slide 31
Imposing conditions
m = 1…M
microphones
d = 1…D
directions
Applying the filter matrix H to the measured impulse responses C, the system should behave as a virtual microphone with wanted directivity
h1(t)
h2(t)
hM(t)
pd(t)
Target function
c1,d(t)
AM,v
δ(t)
A1,v
δ(t)
A2,v
δ(t)
But in practice the result of the filtering will never be exactly equal to the prescribed functions pd…..
c2,d(t)
cM,d(t)

## Slide 32
Least-squares solution
We compare the results of the numerical inversion with the theoretical response of our target microphones for all the D directions, properly delayed, and sum the squared deviations for defining a total error:
The inversion of this matrix system is now performed adding a regularization parameter b, in such a way to minimize the total error (Nelson/Kirkeby approach):
It revealed to be advantageous to employ a frequency-dependent regularization parameter bk.
P

## Slide 33
regularization parameter bk
At very low and very high frequencies it is advisable to increase the value of b.

## Slide 34
Polar patterns of virtual microphones:
From OMNI to CARDIOIDS up to 6th order
Inputs:
  684 IRs, 2048 samples long
  Number of virtual microphones (32 max)
  Directivity of each virtual microphone
  Azimuth and elevation of each virtual microphone
IRs Matrix inversion
Output: FIR filters matrix
FIRs matrix
✕
Capsules’ signals
=>
Virtual mics
Design of the FIR filters
Notes: With a Matlab script we can perform the matrix inversion…
We choose the 4th order cardioids because they are the right compromise for covering the sphere without overlaps of their directivity.
34

## Slide 35
Anechoic measurements
A large anechoic room was employed for full-range measurements
A computer-controlled turntable was employed for rotation at fixed angular steps
The AURORA software was employed for generating the test signals and the control pulses for the turntable
ESS (Exponential Sine Sweep) test signal
The loudspeaker response was measured with a class-0 B&K microphone, and a suitable inverse filter applied to the test signal

## Slide 36
Subsequent rotations of the probe along a meridian, after selecting the meridian by manual rotation of the support.
Support for rotating the probe
Reduced angular resolution for shortening measurement times
Angular step: 10° x 10° N. of measurements: 684 (36 meridians x 19 parallels, including the poles) ESS signal duration: 10 sec Total measurmenet time: approximately 3 hours
Measurements on the whole sphere

## Slide 37
Small angular steps
These are the verification measurements, employed for checking the polar responses of the virtual microphones
Angular step: 5° N. of measurements: 72 ESS signal duration: 10 seconds Total measurement time: approximately 18 minutes
Measurements in the horizontal plane

## Slide 38
The real-time microphone system
The “Black box” runs currently also on the laptop, in background, employing the open-source convolution engine BruteFIR
The Laptop operates with a GUI written in Python, and controlled with a mouse or a joystick
A panoramic camera provides the background live video imaging

## Slide 39: Hardware for 360° video
A 2 Mp hires Logitech webcam is mounted under a parabolic mirror, inside a Perspex tube
The video stream from the Logitech webcam is processed with a realtime video-unwrapping software, written by Adriano Farina in “Processing”, a Java-based programming language and environment
It is possible to record the unwrapped video stream to a standard MOV file

## Slide 40: Video unwrapping
Unwrapped image
Original image

## Slide 41: Video Sample: ScreenRecording

## Slide 42: Video Sample: ScreenRecording

## Slide 43: Example of post-processing with 7 fixed microphones
La Bohème
Theater Regio Turin
20 may 2010
Notes: Innovazioni Tecnologiche Audio
01/03/2010
Leonardo Scopece
43

## Slide 44: Video Sample: Boheme

## Slide 45
3) Spatial PCM Sampling
Whilst Sherical Harmonics are the “spatial” equivalent of the Fourier analysis of a wavefront, we can use our “virtual microphone” approach for synthesizing 32 ultradirective microphones, representing the whole spatial information as a number of “spatial pulses” (PCM, pulse code modulation)
1
2
3
32
32 virtual ultradirective microphones
Notes: [SUI DISEGNI]
For the horizontal polar we synthesize 24 virtual microphones and for the 3D map we created 32 virtual microphones in the direction of the capsules.
45

## Slide 46
3) Spatial PCM Sampling
Comparison of PCM sampling of a waveform and of a spatial sound distribution
Notes: [SUI DISEGNI]
For the horizontal polar we synthesize 24 virtual microphones and for the 3D map we created 32 virtual microphones in the direction of the capsules.
46

## Slide 47
3) Spatial PCM Sampling
Fourier expansion of a waveform and of a spatial sound distribution
Notes: [SUI DISEGNI]
For the horizontal polar we synthesize 24 virtual microphones and for the 3D map we created 32 virtual microphones in the direction of the capsules.
47

## Slide 48
Spatial PCM Sampling
Coverage of the spherical panorama with the 32 ultradirective microphones
Notes: [SUI DISEGNI]
For the horizontal polar we synthesize 24 virtual microphones and for the 3D map we created 32 virtual microphones in the direction of the capsules.
48

## Slide 49
SPS realtime processing
Xvolver is employed for generating the 32 virtual microphones
Notes: The aim of the post processing is a movie representing the behaviour of the sound through a polar plot of the sound levels in the horizontal plane and a mesh map of the levels on a 360°x180° picture of the room.
At first we import the wav files containing the Impulse Responses obtained from the 32 virtual microphones.

## Slide 50
SPS room impulse responses
Sala dei Concerti
(Casa della Musica - Parma)
Teatro “La Scala”
(Milano)
Notes: For the new session of measurements we used two different kind of musical space: a concert hall and a famous Italian opera theatre.
50

## Slide 51
Eigenmike® probe as receiver
Laptop as recorder
“Lookline” Dodecahedron as omni- directional source
Sine sweep as test signal
Measurement details
Notes: In “La Scala Theatre” the dodecahedron source was placed 1m off the center of the stage and a set of points was chosen for the receiver (Figure 11). For both the theatres, in correspondence of the receivers, a panoramic 360° picture was taken with the aim of creating on it the dynamic map of the sound levels. [MOSTRATE NELLA SLIDE SUCCESSIVA]
51

## Slide 52
Notes: Here we have the two panoramic pictures.
52

## Slide 53
Teatro “La Scala”: 4 kHz

## Slide 54
“Sala dei Concerti”: 4 kHz

## Slide 55
16-loudspeakers playback system
From Virtual Microphones to speaker feeds
EigenmikeTM
Matrix of 32x16 FIR filters
32 virtual microphone signals y
16 speaker feeds s

## Slide 56
Characterization of playback system
The EigenmikeTM is placed in the center of the loudspeaker rig, and the transfer functions [k] are measured from each loudspeaker to each of the 32 virtual microphones.
Then we impose that the resulting signals {yout} are identical to the virtual microphone signals recorded by the Eigenmike in the original room {y}:
And consequently we solve for the unknown filters [f]
k1
k2
kR
Virtual microphone signals yout

## Slide 57
From Virtual Microphones to speaker feeds
3D Listening Rooms at ISVR
(Southampton, UK) – 40 loudspeakers
and at Casa della Musica, (Parma, ITALY)
16 loudspeakers

## Slide 58: Locations of loudspeakers
Horizontal Ambisonics octagon
Ambisonics 3D cube
Standard Stereo
Frontal Stereo-Dipole
Rear Stereo Dipole
Upper Stereo Dipole

## Slide 59
From Virtual Microphones to speaker feeds
WFS ROOM “Sala Bianca” at Casa del Suono, (Parma, ITALY)
This room is equipped with 176 loudspeakers controlled by a cluster of 4 computers

## Slide 60
From Virtual Microphones to speaker feeds
WFS ROOM “Sala Bianca” at Casa del Suono, (Parma, ITALY)
is now also equipped with 4 projectors for 360 immersive video

## Slide 61
Conclusions
Our new FIR-based virtual microphone technology permits to:
Employing traditional 1st order Ambisonics microphones for localizing with great accuracy the direction-of-arrival of room reflections
Employing state-of-the-art spherical microphone arrays equipped with 32 capsules for recording concerts or other events, and even for real-time broadcasting applications (up to 7 virtual microphones in realtime with direct synthesis).
Perform a complete spatial analysis of the sound field employing the novel SPS approach (with 32 ultradirective virtual microphones)
SPS (Spatial PCM Sampling) allows for creating video animations of the spatial distribution of the sound arriving at the receiver
The virtual microphone signals can be also designed for feeding a 3D loudspeaker array (3D spatial sound reproduction)
Notes: This is a first step in the research, a lot of work has to be done:
for example we should find out a good method for calibrating the probe and giving to the user the absolute level of the sound he is watching in the movie.
A Matlab script is not optimal for a massive use. We’d like to create a VST plugin or a standalone software for give a better usability
We should use an IP camera for taking panoramic photo because the actual process consist in the union of multiple shots at different angles… A waste of time.

## Slide 62: Linear array
16 omnidirectional mikes mounted on a 1.2m aluminium beam, with exponential spacing
16 channels acquisition system:
2 Behringer A/D converters + RME
Hammerfall digital sound card
Sound recording with Adobe Audition
Filter calculation, off-line processing and visualization with Aurora plugins

## Slide 63: Linear array - calibration
The array was mounted on a rotating table, outdoor
A Mackie HR24 loudspeaker was used
A set of 72 impulse responses was measured employing Aurora plugins under Adobe Audition (log sweep method) - the sound card controls the rotating table.
The inverse filters were designed with the local approach (separate inversion of the 16 on-axis responses, employing Aurora’s “Kirkeby4” plugin)

## Slide 64: Linear array - polar plots

## Slide 65: Linear array - practical usage
The array was mounted on an X-Y scanning apparatus
a Polytec laser vibrometer is mounted along the array
The system is used for mapping the velocity and sound pressure along a thin board of “resonance” wood (Abete della val di Fiemme, the wood employed for building high-quality musical instruments)
A National Instruments board controls the step motors through a Labview interface
The system is currently in usage at IVALSA (CNR laboratory on wood, San Michele all’Adige, Trento, Italy)

## Slide 66: Linear array - practical usage
The wood panel is excited by a small piezoelectric transducer
When scanning a wood panel, two types of results are obtained:
A spatially-averaged spectrum of either radiated pressure, vibration velocity, or of their product (which provides an estimate of the radiated sound power)
A colour map of the radiated pressure or of the vibration velocity at each resonance frequency of the board

## Slide 67: Linear array - test results (small loudspeaker)

## Slide 68: Linear array - test results (rectangular wood panel)
SPL (dB)
velocity (m/s)
SPL (dB)
velocity (m/s)

## Slide 69: Planar array (“acoustic camera”)
24 omnidirectional mikes mounted on a 1m square foldable wooden baffle with an optimized random disposition
24 channels acquisition system:
Behringer A/D converters + RME
Hammerfall digital audio card
Filters calculation, off-line processing and visualization with MATLAB

## Slide 70: Random array vs. Circular array

## Slide 71: Circular array vs. Random array
The optimal randomized positions were found by running 10000 Matlab simulations, and chosing the one providing the better peak-to-noise ratio
Simulated matrix inversion - 3 kHz

## Slide 72: Beamforming vs. Inverse filters
Random Array - Matrix inversion - 1 kHz

## Slide 73: Effect of the regularization parameter
e = 0.01
e = 0.1
Random Array - Matrix Inversion - 5 kHz

## Slide 74: Indoor application (source localisation)
The array is equipped with a webcam
The filtering process discriminates each spherical wave (Tr’k(t)) coming by the pixels of a virtual screen placed on the plane where machine to be tested lyes
At each pixel is associated the A-weighted equivalent level (LAeq, in dB) of each soundtrack extracted
The dB(A) color map is matched and superimposed to the webcam image

## Slide 75: Outdoor application
The array is placed behind a noise barrier
The colour map of the SPL shows the leakage under the barrier

## Slide 76: Real time processing: work on progress
VST Host:
Audiomulch, Bidule, MaxMSP
“X-volver”: VST Plugin
24-channels inputs
M-channels output
MAP
ARRAY

## Slide 77: “X-volver” VST plugin
1 output
X-Volver
16 inputs

## Slide 78: 3D arrays
DPA-4 A-format microphone
4 closely-spaced cardioids
A set of 4x4 filters is required for getting B-format signals
Global approach for minimizing errors over the whole sphere